| IPsec VPN Profile for DBM-SRV-2007 |
| --- |
|  | DatabaseMart End | Vendor End |
| VPN Device | Cisco ASA 5505 | ？ |
| Endpoint IP Address | xx.xx.xx.xx | ？ |
| Local Networks | 10.10.10.0/24 | ？ |
| IKE Setting | IKE Encryption (DES, 3DES, AES-128, AES-192, AES-256) | AES-256 | AES256 |
|  | Authentication Method (MD5, SHA) | SHA1 | SHA 1 |
|  | Diffie-Helman Group (1,2,5) | 5 | 5 |
|  | Security Association Lifetime (sec) | 28800 | 28800 |
|  | Pre-Shared Secret | ？ |
| IPsec Setting | IKE Encryption (DES, 3DES, AES-128, AES-192, AES-256) | AES256 | AES256 |
|  | Authentication Method (None, MD5, SHA) | SHA1 | SHA 1 |
|  | Perfect Forward Secrecy | Disabled | Disabled |
|  | Security Association Lifetime (sec) | 3600 | 3600 |